## Slide 1
Gateway Middle End HW Test on production line for the 2G model
V.1.0 16/07/2020

## Slide 2
Overview – HW part
On the following slides you will find the description of the method to program the FW and test the HW on the gateway middle end WiFi.
The test HW is described on the next slide and are made using this HW list : n.1 pcs from RS components RS 174-3234 Shield relè 3.0 for Shield Arduino/Seeeduino Relay Shield 3.0 n.1 pcs from RS components RS 715-4081 Arduino Uno Rev.3
n.1 pcs from RS components RS 429-284 USB/TTL 3V3 converter n.1 pcs from RS components RS 429-278 USB/TTL 5V converter
n.1 pcs power supply 230V to 12VAC 1°
The same HW are widely available on Internet from other vendors.
The system require a test bed to connect with nails some test points to the test machine.

## Slide 3
Overview – SW part
About the SW to drive the test
- we have made a demo program to perform the programmation and test of the device, is written in C# to have a simple user interface, some part of test program will be in Python due to the fact that these part are developed by Espressif.
- Below the documentation of
1 - the serial protocol used to interact with the HW I/O module.
2 - documentation about the serial response of the GME in test mode
ie. format of the response about MAC address value, connection test etc.
3 - the test list
- Some exclusion;
The test system is not complete because some pieces are impossible to made by CAREL :
5 - Label print; the mechanism to print is in charge to USR, in fact depends on printer type, template definition, and so on.
6 - Serial Number; typically the S/N is retrieved by a call to the factory management system that return the data,
so that, only USR know how it works. Fortunately this data is present only in the label and not programmed inside the GME, so is possible to call an external program to retrieve it and print the label.
At the end USR have two possibility :
a - read the documentation and implements the test suite with the scripting method they like,
and use the test demo SW as an implementation reference.
b - complete the CAREL SW with the missing parts of point 5, 6

## Slide 4
Arduino Uno + 4 Relè shield
GME - 2G
under test
Power Supply 12VDC
PC
USB/TTL 5V Adapter
TTL port
RX/TX/GND/ 5VDC
USB n.2
USB n.1
R3 OUT
TP5
R3 IN
GND
R1 OUT
USB/RS485 Adapter
USB n.3
RS485
R1 IN
+ Power Connector
TP_3V3
A0 in
22,1K 1%
11K 1%
R2 IN
R2 OUT
230VAC
Button
R4 IN
R4 OUT
TP_EN
2G Cellular Network or Base Station Simulator
Test HW block diagram

## Slide 5
Arduino Uno serial protocol
The Arduino Uno is programmed with a simple program able to receive some commands through the serial port. The serial port parameters are : 115200/N/8/1
The commands are simple ASCII string terminate with ‘\n’ ie. ‘A0\n’, so is very easy to make a program to interact with it.
The available commands are :
Command | Answer from Arduino | 
A0 | None | Open relè n.1
A1 | None | Close relè n.1
B0 | None | Open relè n.2
B1 | None | Close relè n.2
C0 | None | Open relè n.3
C1 | None | Close relè n.3
D0 | None | Open relè n.4
D1 | None | Close relè n.4
V | V=xxxx where xxxx is the RAW number from the AD converter | Read voltage

## Slide 6
Gateway Middle End (GME) test FW
The GME have a test FW inside, if during the power on or a reset, the test point TP5 is connected to ground the GME start in test mode. In test mode the GME emit some message from the TTL port, all the messages are terminated with ‘\n’. The serial port parameters are : 115200/N/8/1 The GME in test mode try to read with Modbus protocol through the RS485 port the HR n.1 of a connected device, in this case a simulator.
The serial port of simulator must be set to : 19200/N/8/1
In the next slide the list of returned message.

## Slide 7
Gateway Middle End (GME) test FW
In the table below the list of the message :
Output string | Note
IMEI=aabbccddeeff | The IMEI of the device
SIM=xx | OK correctly installed SIM FAIL NOT installed properly
GSM=xx | OK able to see the selected operator FAIL NOT able to see the selected operator means antenna trouble
HR=xxxx | Value of Holding register n.1 read from RS485 port

## Slide 8
HW Pre-requisite
To program the Arduino board install the Arduino IDE at this link https://www.arduino.cc/en/main/software and follow this steps
Launch the Arduino IDE
File > Open the file > C780_HW_Test_Arduino_FW.ino
Choose on Port > the serial port of the Arduino Uno board
Choose from Board > «Arduino/Genuino Uno» [normally the default]
Press the button
Wait the End of the operation
To quick check if the board is programmed right :
Press the button
A terminal appear check at the botton of the window that the baudrate is 115200
In the top box type «V» + Enter
The board respond «V=0» or similar answer

## Slide 9
SW Pre-requisite
In order to run the SW the following prerequisite are needed
Modbus_PC_Simulator
- Python V.2.7.x
- pymodbus (https://pymodbus.readthedocs.io/en/latest/readme.html#installing)
- pyserial (https://pypi.org/project/pyserial/)
CAREL_GME_Test
Launch the program CAREL_GME_Test.exe and download and install the requested .NET Framework
After the installation follow this steps:
Edit with notepad the file CAREL_GME_Test_CFG.ini and set the COM ports according with your HW configuration
Edit the operator name returned by the command AT+COPS, the easy way to determinate it is by launch the program initially with a dummy operator «testoperator», launch the test that will fail obviously but you see the answer in the monitoring window copy&paste the operator name and substitute the «testoperator» string.
Launch the CAREL_GME_Test.exe go to the panel on the right «Manual» you will find a series of button check the HW connections with the aid of these buttons.

## Slide 10
Test sequence
All relè open
Close Relè Button > Wait 500 ms
Close Relè Power > Wait 500 ms
Close Relè EN
Ask the operator "Is the power led ON ?“ if yes go ahead otherwise stop the test
Reas the 3V3 voltage level, if within the limits go ahead otherwise stop the test
Open Relè EN > Wait 1000 ms
Open Relè Button > wait 1000 ms
Run the FW programming routine
Check if the programmation is ok and go ahead otherwise stop the test
Initialize the PC serial connected to the TTL port
Ask the operator "Take a look to the status led to see if blink“?“
Close Relè EN > Wait 500 ms
Close Relè TP5 > Wait 500 ms
Open Relè EN
Ask the operator "LED STATUS TEST", "The status led have blinked green/red ?" if yes go ahead otherwise stop the test
Read the MAC address via serial port, if yes go ahead otherwise stop the test
Check the SIM presence, if success go ahead otherwise stop the test
Try to connect to find the 2G operator ? if success go ahead otherwise stop the test
Try to read value through the RS485 port ?" if success go ahead otherwise stop the test
End of test