## Slide 1
Gateway Middle End HW Test on production line
V.1.2 02/07/2020

## Slide 2
Overview – HW part
On the following slides you will find the description of the method to program the FW and test the HW on the gateway middle end WiFi.
The test HW is described on the next slide and are made using this HW list : n.1 pcs from RS components RS 174-3234 Shield relè 3.0 for Shield Arduino/Seeeduino Relay Shield 3.0 n.1 pcs from RS components RS 715-4081 Arduino Uno Rev.3
n.1 pcs from RS components RS 429-284 USB/TTL 3V3 converter n.1 pcs from RS components RS 429-278 USB/TTL 5V converter
n.1 pcs power supply 230V to 12VAC 1°
The same HW are widely available on Internet from other vendors.
The system require a test bed to connect with nails some test points to the test machine.

## Slide 3
Overview – SW part
About the SW to drive the test
- we have made a demo program to perform the programmation and test of the device, is written in C# to have a simple user interface, some part of test program will be in Python due to the fact that these part are developed by Espressif.
- Below the documentation of
1 - the serial protocol used to interact with the HW I/O module.
2 - documentation about the serial response of the GME in test mode
ie. format of the response about MAC address value, connection test etc.
3 - the test list
- Some exclusion;
The test system is not complete because some pieces are impossible to made by CAREL :
5 - Label print; the mechanism to print is in charge to USR, in fact depends on printer type, template definition, and so on.
6 - Serial Number; typically the S/N is retrieved by a call to the factory management system that return the data,
so that, only USR know how it works. Fortunately this data is present only in the label and not programmed inside the GME, so is possible to call an external program to retrieve it and print the label.
At the end USR have two possibility :
a - read the documentation and implements the test suite with the scripting method they like,
and use the test demo SW as an implementation reference.
b - complete the CAREL SW with the missing parts of point 5, 6

## Slide 4
Arduino Uno + 4 Relè shield
GME
under test
Power Supply 12VDC
PC
USB/TTL 5V Adapter
TTL port
RX/TX/GND/ 5VDC
USB n.2
USB n.1
R3 OUT
TP5
R3 IN
GND
R1 OUT
USB/RS485 Adapter
USB n.3
RS485
R1 IN
+ Power Connector
TP_3V3
A0 in
22,1K 1%
11K 1%
R2 IN
R2 OUT
230VAC
Button
R4 IN
R4 OUT
TP_EN
TEST ACCESS POINT SSID «TEST_AP» PWD «12345678»
Test HW block diagram

## Slide 5
Arduino Uno serial protocol
The Arduino Uno is programmed with a simple program able to receive some commands through the serial port. The serial port parameters are : 115200/N/8/1
The commands are simple ASCII string terminate with ‘\n’ ie. ‘A0\n’, so is very easy to make a program to interact with it.
The available commands are :
Command | Answer from Arduino | 
A0 | None | Open relè n.1
A1 | None | Close relè n.1
B0 | None | Open relè n.2
B1 | None | Close relè n.2
C0 | None | Open relè n.3
C1 | None | Close relè n.3
D0 | None | Open relè n.4
D1 | None | Close relè n.4
V | V=xxxx where xxxx is the RAW number from the AD converter | Read voltage

## Slide 6
Gateway Middle End (GME) test FW
The GME have a test FW inside, if during the power on or a reset, the test point TP5 is connected to ground the GME start in test mode. In test mode the GME emit some message from the TTL port, all the messages are terminated with ‘\n’. The serial port parameters are : 115200/N/8/1 The GME in test mode try to read with Modbus protocol through the RS485 port the HR n.1 of a connected device, in this case a simulator.
The serial port of simulator must be set to : 19200/N/8/1
In the next slide the list of returned message.

## Slide 7
Gateway Middle End (GME) test FW
In the table below the list of the message :
Output string | Note
MAC=aabbccddeeff | The MAC address of the device without separator «:»
STA=xxxxxxx | STA=CONNECTED STA=DISCONNECTED the GME try to connect to an AP with SSID «GME_TEST» and PWD «12345678» in case of success return CONNECTED.
HR=xxxx | Value of Holding register n.1 read from RS485 port

## Slide 8
Test sequence Not completed will update at the end of development
All relè open
Close R4
Close R2
Close R1
Wait 0,5 sec.
Measure TP_3V3, if >= 3,1 and <= 3,5 if yes go ahead otherwise stop the test
Open R4
Wait 1 sec
Open R2
Call the routine to transfer the FW to the device, wait the end, check if ok go ahead otherwise stop the test
Ask the operator to Press a button on a messagebox an take a look to the status led, «Press ..»
Close R2, wait 0,5 sec. , Open R2 (reset)
Are the led status blinking ? if ok go ahead otherwise stop the test
Retrieve the MAC address from the device
Check if the RS485 works
End of test

## Slide 9
HW Pre-requisite
To program the Arduino board install the Arduino IDE at this link https://www.arduino.cc/en/main/software and follow this steps
Launch the Arduino IDE
File > Open the file > C780_HW_Test_Arduino_FW.ino
Choose on Port > the serial port of the Arduino Uno board
Choose from Board > «Arduino/Genuino Uno» [normally the default]
Press the button
Wait the End of the operation
To quick check if the board is programmed right :
Press the button
A terminal appear check at the botton of the window that the baudrate is 115200
In the top box type «V» + Enter
The board respond «V=0»

## Slide 10
SW Pre-requisite
In order to run the SW the following prerequisite are needed
Modbus_PC_Simulator
- Python V.2.7.x
- pymodbus (https://pymodbus.readthedocs.io/en/latest/readme.html#installing)
- pyserial (https://pypi.org/project/pyserial/)
CAREL_GME_Test
Launch the program CAREL_GME_Test.exe and download and install the requested .NET Framework
After the installation follow this steps:
Edit with notepad the file CAREL_GME_Test_CFG.ini and set the COM ports according with your HW configuration
Launch the CAREL_GME_Test.exe go to the panel on the right «Manual» you will find a series of button check the HW connection with the aid of these buttons.