## Slide 1
Gateway Middle End HW Test on production line
V.1.0 30/06/2020

## Slide 2
Overview
On the following slides you will find the description of the method to program the FW and test the HW on the gateway middle end WiFi.
The test HW is described on the next slide and are made using this HW list : n.1 pcs from RS components RS 174-3234 Shield relè 3.0 for Shield Arduino/Seeeduino Relay Shield 3.0 n.1 pcs from RS components RS 715-4081 Arduino Uno Rev.3
n.1 pcs from RS components RS 429-284 USB/TTL 3V3 converter n.1 pcs from RS components RS 429-278 USB/TTL 5V converter
n.1 pcs power supply 230V to 12VAC 1°
The same HW are widely available on Internet from other vendors.

## Slide 3
Arduino Uno + 4 Relè shield
GME
under test
Power Supply 12VDC
PC
USB/TTL 5V Adapter
TTL port
RX/TX/GND/ 5VDC
USB n.2
USB n.1
R3 OUT
TP5
R3 IN
GND
R1 OUT
USB/RS485 Adapter
USB n.3
RS485
R1 IN
+ Power Connector
TP_3V3
A0 in
22,1K 1%
11K 1%
R2 IN
R2 OUT
230VAC
Button
R4 IN
R4 OUT
TP_EN
TEST_AP

## Slide 4
Arduino Uno serial protocol
The Arduino Uno is programmed with a simple program able to receive some commands through the serial port. The serial port parameters are : 115200/N/8/1
The commands are simple ASCII string terminate with ‘\n’ ie. ‘A0\n’, so is very easy to make a program to interact with it.
The available commands are :
Command | Answer from Arduino | 
A0 | None | Open relè n.1
A1 | None | Close relè n.1
B0 | None | Open relè n.2
B1 | None | Close relè n.2
C0 | None | Open relè n.3
C1 | None | Close relè n.3
D0 | None | Open relè n.4
D1 | None | Close relè n.4
V | V=xxxx where xxxx is the RAW number from the AD converter | Read voltage

## Slide 5
Gateway Middle End (GME) test FW
The GME have a test FW inside, if during the power on, the test point TP5 is connected to ground the GME start in test mode. In test mode the GME emit some message from the TTL port, all the messages are terminated with ‘\n’. The serial port parameters are : 115200/N/8/1 The GME in test mode try to read with Modbus protocol through the RS485 port the HR n.1 of a connected device, in this case a simulator.
The serial port of simulator must be set to : 19200/N/8/1
In the next slide the list of returned message.

## Slide 6
Gateway Middle End (GME) test FW
In the table below the list of the message :
Output string | Note
MAC=aabbccddeeff | The MAC address of the device without separator «:»
STA=xxxxxxx | STA=CONNECTED STA=DISCONNECTED the GME try to connect to an AP with SSID «GME_TEST» and PWD «12345678» in case of success return CONNECTED.
HR=xxxx | Value of Holding register n.1 read from RS485 port

## Slide 7
Test sequence DA AGGIORNARE
All relè open
Close R4
Close R2
Close R1
Wait 1 sec.
Measure TP_3V3, if >= 3,1 and <= 3,5 if yes go ahead otherwise stop the test
Open R4
Wait 1 sec
Open R2
Call the routine to transfer the FW to the device, wait the end, check if ok go ahead otherwise stop the test
Ask the operator to Press a button an take a look to the status led, «Press ..»
Close R2, wait 1 sec. , Open R2 (reset)
Are the led status blinking ? if ok go ahead otherwise stop the test